## Slide 1
Geographic Information System
PRESENTED BY
ANKIT GUPTA
ASSISTANT PROFESSOR
DEPARTMENT OF CIVIL ENGINEERING
UNITED COLLEGE OF ENGINEERING AND RESEARCH, PRAYAGRAJ

## Slide 2: What is GIS?

## Slide 3: Geographical Information System
o A set of tools for
Collecting
•
•
•
•
Storing Manipulating Retrieving
Transforming and Display of Spatial Data from the Real World

## Slide 4: What is a GIS?
GEOGRAPHIC
implies that locations of the data items are known, or can be calculated, in terms of Geographic coordinates (Latitude, Longitude)
INFORMATION
implies that the data in a GIS are organized to yield useful knowledge, often as colored maps and images, but also as statistical graphics, tables, and various on-screen responses to interactive queries.
SYSTEM
implies that a GIS is made up from several inter-related and linked components with different functions. Thus, GIS have functional capabilities for data capture, input, manipulation, transformation, visualization, combinations, query, analysis, modelling and output.

## Slide 5: What is GIS?
GIS = Geographic Information System
  Links databases and maps
  Manages information about places
  Helps answer questions such as:
    Where is it?
    What else is nearby?
    Where is the highest concentration of ‘X’?
    Where can I find things with characteristic ‘Y’?
    Where is the closest ‘Z’ to my location?

## Slide 6: What is GIS?
6
A technology
– hardware & software tools
An information handling strategy
The objective: to improve overall decision making

## Slide 7: GIS: a formal definition
7
“A system for capturing, storing, checking, integrating, manipulating, analysing and displaying data which are spatially referenced to the Earth. This is normally considered to involve a spatially referenced computer database and appropriate applications software”

## Slide 8: Why is GIS unique?
8
GIS handles SPATIAL information
– Information referenced by its location in space
GIS makes connections between activities based on spatial proximity

## Slide 9: GIS Process
Capture Data
Register Map Base
Interpret Data
Convert Data to Digital Format
Store Data in Computer
Process Data
Display Results

## Slide 10: Images
GIS
System
Spatial Data Base
Attribute Data Base
Cartographic Display System
Geographic Analysis
System
Map Digitizing System
Image Processing System
Statistical Analysis
System
Database Management System
Maps
Maps
Statistical Reports
Statistics Tabular Data

## Slide 11: GIS Areas
Geo Sciences Civil Engineering Transportation Natural resources
Geology & Geophysics Environment Planning Administration Management
Business
Remote Sensing Image processing
Urban & Rural Development
Floods , Disasters Oil exploration
Mines Surveys
Watershed management
Tourism Communications

## Slide 12: Softwar es
Digital Image Processing
 ERDAS Imagine
 ER Mapper
 ILWIS
 ENVI
 PCI Geomatica









GIS
ARC INFO
ArcGIS MapInfo GRASS
Geomedia Geoconcept WIN GIS
Microstation AutoCAD
ArcView image analysis
  TNTMIPS
  Ecognition

## Slide 14: Internal users
Data management
output
input
analysis
GIS
data base
Internal data base
Internal management
External management
External user
External
data base

## Slide 16: FUNCTIONS OF GIS

## Slide 19: Application of GIS
GIS used in multiple disciplines:
Agriculture
Archaeology Architecture/Landscape Arch. Business
Computer Science Environmental Science
Engineering Journalism Military Science
Natural Resource Management
Geography Geology Meteorology Oceanography Law Enforcement Public Health History Sociology
Urban/Regional Planning

## Slide 20: Agriculture
Farm management
Pest/Disease tracking
Crop monitoring
Yield prediction
Soil analysis

## Slide 21: Natural Resource Management
Forestry
Ecology
Mining
Petroleum
Water Resources

## Slide 22: Planning and
Economic Development
Land Use/Zoning
Emergency Preparedness
Population Forecast
Market Analysis
Property Tax Assessment
Transportation

## Slide 23: GIS: A Framework for Understanding and Managing Our Earth
Holistic Comprehensive Systematic Analytic
Visual
Measuring
Organizing Analyzing Modeling
Applying
Planning Managing Acting
Geographic Knowledge
Creating

## Slide 24: Geography matters
Today’s challenges require geographic approach
•
•
•
•
•
•
•
•
Climate Change Urban Growth
Sustainable Agriculture Water Quality and Availability
International and National Security
Energy
Epidemiology/Disease Tracking
Natural Hazards: Seismicity, Weather Events

## Slide 25: GIS as Infrastructure
Because GIS is used in many departments, coordination is needed
  Software licensing
  Instruction
  Data

## Slide 26: GIS as infrastructure
Data is greatest expense
  Previously: Data scattered in multiple departments, not coordinated
  Future: Data accessible anywhere, GIS portal and Web services facilitate sharing
Libraries / Data Centers key
  GIS data has unique characteristics

## Slide 27: Civil Engineering Applications
Fundamentals of GIS
Transportation
Watershed analysis
Remote sensing

## Slide 28: Location-Allocation Inputs
Fundamentals of GIS
Customer or demand locations
Potential site locations and/or existing facilities
Street network or Euclidean distance
The problem to solve

## Slide 29: Location-Allocation Outputs
Fundamentals of GIS
The best sites
The optimal allocation of demand locations to those sites
Lots of statistical and summary information about that particular allocation

## Slide 30: Vehicle Routing
Fundamentals of GIS
(From , ESRI)

## Slide 31: Other Transportation Applications
Fundamentals of GIS
Planning & locating new roadway corridors
(from NCRST-E)

## Slide 32: Transportation – Emergency Operations
Fundamentals of GIS
Transportation maps are critical
Disaster response plans can be developed
Outside computer models used for advance warnings
Land use maps enhance emergency operations

## Slide 33: Watershed Characterization
Fundamentals of GIS
Relate physical characteristics to water quality & quantity
Data – land use & land cover, geology, soils, hydrography & topography – related to hydrological properties

## Slide 34: Watershed
Fundamentals of GIS
Applications
Estimate the magnitude of high-
flow events, the probability of low- flow events
Determine flood zones
Identify high-potential erosion areas
For example, BASINS, HEC-RAS, MIKE11 models integrated with
GIS

## Slide 35: GIS DATA AND SOURCES

## Slide 36: Data Structure
GIS
GRAPHIC
ALPHA NUMERIC
VECTOR
RASTER
CO-ORDINATE
SYSTEM
IMAGE
AREAL PHOTOGRAPH
REMOTE SENSED SCANNED IMMAGES
SPATIAL
NON-SPATIAL/
ATTRIBUTE
NON-SPATIAL/
ATTRIBUTE

## Slide 37: Maps And Map Elements
Maps are graphic representation of our perception of the world around us. They represent cartographic interpretation and simplification of reality.
Maps provide two types of information
o o
Locational information Spatial Relationships

## Slide 38: Maps contains features such
as………
Point, Line, Area and Surface
Maps contain POINT features, LINE features and AREA features
Point Features :- wells, control points, sample sites, fire stations
Line Features :- roads, hydro lines, rivers, contour lines,
Area Features:-urban areas, water bodies, soil/rock units, forest areas

## Slide 39: Point Features
Spatially distributed entities, activities or events
Points have a single geographic coordinate such as:
  Tree
  Traffic accident
  Lamp post

## Slide 41: Line Features
Spatially distributed entities, activities or events
Lines (Arcs) are a series of geographic coordinates joined to form a line such as:
  Road
  Stream
  Railway

## Slide 43: Area Features
Spatially distributed entities, activities or
o events
Areas (Polygons) are a series of geographic coordinates joined together to form a boundary such as:
  Lake
  Soil types

## Slide 45: GIS Data Formats
There are two formats used by GIS systems to store and retrieve geographical data:
  Raster
  Vector

## Slide 46: SPATIAL DATA
Raster
Vector
Data Model And Structure
RASTER MODEL
VECTOR MODEL

## Slide 47: Raster Format
Data are divided into cell, pixels, or elements
Cells are organized in arrays
Each cell has a single value
Row and Column Numbers are used to identify the location of the cell within the array.
Perhaps the most common example of raster data is a digital image.

## Slide 48: Raster Data
A grid (or raster) system stores data as a string of characters in which each character represents a location.
The basic data unit is a cell or Pixel Each cell/Pixel is assigned only one value
An array of Pixels form the entity-Point, Line, Area and surface
The shape and size of the array determines the basic Resolution
Polygons can be formed indicating areas of homogeneous characteristics

## Slide 50: Vector Format
Data are associated with points, lines, or boundaries enclosing areas
Points are located by coordinates
Lines are described by a series of connecting vectors (line segments described by the coordinates of the start of the vector, its direction, and magnitude or length).
Areas or polygons are described by a series of vectors enclosing the area.

## Slide 51: Vector Format
Any number of factors or attributes can be associated with a point line or polygon.
Data are stored in two files:
  a file containing location information
  a file containing information on the attributes
A third file contains information needed to link positional data with their attributes.

## Slide 52: Vector Data
A vector system usually stores data as coordinates.
For example Each uniform area is surrounded by a set of straight line segments called vectors.
In a vector based system every point is recorded by a pair of x and Y coordinates.
Straight line segments called vectors are displayed to indicate line based data ( roads rivers wells)
The x-y coordinates at the end of each vector can be digitized and stored.
Most spatial features can be displayed as: - Points- Line- Polygons

## Slide 54: Vector and Raster Representation of Point Map Features
Map Feature
GIS Vector Format
GIS Raster Format
(X,Y)
Coordinate in space
Cell Located in an Array

## Slide 55: Vector and Raster Representation of Line Map Features
Map Feature
GIS Vector Format
GIS Raster Format

## Slide 56: Vector and Raster Representation of Area Map Features
Map Feature
GIS Vector Format
GIS Raster Format

## Slide 57: Comparison of Raster and Vector Formats
•
•
Raster files are generally very large because each cell occupies a separate line of data, only one attribute can be assigned to each cell, and cell sizes are relatively small.
•
•
Raster
Raster formats are efficient when comparing information among arrays with the same cell size.
Vector
Vector formats are efficient when comparing information whose geographical shapes and sizes are different.
Vector files are much smaller because a relatively small number of vectors can precisely describe large areas and a many attributes can be ascribed to these areas.

## Slide 58: Comparison of Raster and Vector Formats
•
•
Raster
Raster representations are relatively coarse and imprecise
Vector
Vector representations of shapes can be very precise.
Most GIS software can display both raster and vector data. Only a limited number of programs can analyze both types of data or make raster type analyses in vector formats.

## Slide 59: Attribute
data that is assigned to a point, line or area spatial features
Example Attributes…
Stand ID, Compartment No., Vegetation type, Name of the Forest Block, Types of Road, VSS code etc.,
Attributes caDn bae tnuameric or alfa-numeric

## Slide 60: NATURE OF SPATIAL DATA
(GEOGRAPHIC OBJECTS)
•
spatial component
relative position between objects
coordinate system
•
attribute component
– explains spatial objects characteristics
•
spatial relationship
– relationship between objects
•
time component
– temporal element

## Slide 61
Digital data
Maps and
Plans
Paper files
Photogrammetry
Remote Sensing
Field survey
Interviews
GIS Data Sources
Data
Data
Data
Data
GIS

## Slide 62: DATA SOURCES
•
Existing data
digital
map and plan
paper files
  low cost
•
acquisition
remote sensing
photogrammetry
field survey
  high cost

## Slide 63: DATA ACQUISITION
•
spatial component can be obtained by
remote sensing
photogrammetry
survey
•
attribute component can be obtained by
remote sensing/photogrametry
interviews
field visit

## Slide 64: ATTRIBUTE COMPONENT
•
retype from maps, plans or hardcopy files
•
copied from existing digital data

## Slide 65: SPATIAL ACCURACY
•
Precision - indicates how closely several positions fall
in relation to each other
•
Accuracy - is a measure of the closeness of one or
more positions to a position that is known and defined in terms of an absolute reference system.